## Slide 1
Električki avtobusi u gradskom prijevozu
Aleš Klinc, Municipality of Maribor

## Slide 2
Električni avtobusi u gradskom prijevozu
CIVINET WEBINAR, 19.5.2021
MUNICIPALITY OF MARIBOR

## Slide 3
MUNICIPALITY OF MARIBOR
Municipality of Maribor (MOM) is the second largest city in Slovenia and the central local community in the Podravska region. (112000 inhabitants - 20000 students, 15000 schoolchildren), 147 m2
CIVINET WEBINAR, 19.5.2021
MOM is the public decision -making body for transport planning incl. infrastructure and is responsible for public transport infrastructure
Responsible: Public utility and traffic department

## Slide 4
SUMP – adopted by city council in august 2015
- no energent for bus service favorised
Increase quality of service (faster service (15 km/h), headway – 7 minutes on main corridors)
40 new buses (20 for replacement, 20 new)
- SEAP aim reducing the energy consumption of the transport system by 3%
MUNICIPALITY OF MARIBOR – Strategic documents
CIVINET WEBINAR, 19.5.2021

## Slide 5
One municipaliy owned PT operator – MARPROM
21 city bus lines with 230 km total lenght
68 buses (capacity - 1.550 sits, 2.246 stands)
70,6 % diesel buses, 26,4 % CNG, 3 ebus – pedestrian zone, 1 electric hybrid
Avarage age of buses 11,3 in 2014; 5,8 in 2018
121 drivers
2,8 mil km on yearly basis
Budget 6,3 mil. € (Subsidy 4,1 mil. €)
City bus service in Maribor
Standard | Number
EURO 1 | 0
EURO 2 | 0
EURO 3 | 5
EURO 4 | 8
EURO 5 | 12
EURO 5 EEV | 2
EURO 6 | 40
Electric (mini) | 3
SUM | 68
CIVINET WEBINAR, 19.5.2021

## Slide 6: Context information – Maribor‘s efforts for electromobility
first fast-charging station – 2012
56 e-car sharing spots in MB,
180 in Slovenia)
20 fast EV charging stations + 6 Tesla EV chargers
Additional 23 fast EV charging station planned in 2021
62 free parking for EV
AVANT CAR – 100% CAR SHARING system
CIVINET WEBINAR, 19.5.2021

## Slide 7: Context information - Maribor‘s efforts for electric PT
2014 ELIPTIC, activities for electrifying PT (Electrifying PT route 6)
2019 EFFICIENCE,
CIVINET WEBINAR, 19.5.2021

## Slide 8
EXPECTATIONS FROM THE PROJECT ELIPTIC
Best practice examples from other cities (London, Berlin, Madrid, Budapest, Oberhausen, Bremen, Gdynia…)
Costs/savings
Impacts (economic, environmental, operational)
Administrative procedures
Technical characteristic
Transferability
Evidence based approach (scientific view)
Real-life experience
CIVINET WEBINAR, 19.5.2021

## Slide 9: Testing
Hybrid bus (Iveco Urbanway electric hybrid) testing in 2016 –
Since may 2018 in operation
25 % less fuel consumption than diesel/high investment and maintenance cost
EU project ELIPTIC – 2014-2018
CIVINET WEBINAR, 19.5.2021

## Slide 10: Testing
E-bus (Solaris Urbino – full electric) - testing in 2017 –
  average consumption 1,1 kWh/km,
  impact of heating (up to 1,4 kWh/km),
  hilly terrain – no higher consumption E-Bus
E-bus (HEULIEZ IVECO – full electric) – testing in 2019
E-bus (TAM Vero, Mercedes eCitaro, MAN Lions City E) in 2020, 2021
EU project ELIPTIC – 2014-2019
CIVINET WEBINAR, 19.5.2021

## Slide 11
E-bus – experience
- Not succesfull public procurement of 5 plug-in electric buses in 2018
Is the market ready?
MOM started new project EFFICIENCE in 2019
CIVINET WEBINAR, 19.5.2021

## Slide 12
CHALLENGES regarding PT infrastructure
Project EfficenCE, 2019 - 2022
  No common vision on Public transport infrastructure
  Finding optimal relation between batteries size and e-bus charging power/technology (LCC, efficency of the battery systems, additional energy storage for e-bus charges, smart grid)
  no real experience in using of full sustainable energy
  Administrative procedures for E-bus charging building and operating permit may slow down the implementation
  Vandalism
  Gauge (opp charger and oversized transport)
  Influence of weather on operations – cable car (full stop in cases of wind/ heavy rain – 2 to 3 times per year)
  Energy overload at bigger events (e.g worldcup in bike downhill, golden fox FIS SKI WOLRD CUP)
CIVINET WEBINAR, 19.5.2021

## Slide 13
ROLE IN THE PROJECT
MOM
Aim is to partly electrify public transport (bus)
Action Plan of Multipurpose PT infrastructure
Investment in multipurpose PT infrastructure for cable car, e-bus, e-car on the the turning point of bus line 6
University of Maribor; The Faculty of Civil Engineering, Transportation Engineering and Architecture:
Support in the preparation of documentation for MOM
Testing a multipurpose PT infrastrucutre (together with MOM) according to the timetable and e-network stability
CIVINET WEBINAR, 19.5.2021

## Slide 14
CITY/ PT NETWORK MAP – Line 6
TAKING COOPERATION FORWARD

## Slide 15
MAIN ACTIVITIES – PROJECT PARTNER MOM and UMFGPA
Preparation phase MOM, UM FGPA and MARPROM (03.2020)
  investment documentation
  technical feasibility studies (upgrade of cable car substation, identification for e-bus charger and battery power)
  Concept of Multipurpose PT infrastructure
  Building and operation permit/planning permission
  call for tender (end of 2019)
Test phase (12 months leasing)
  incl. construction & connection to the grid works & public launch event (09. 2020)
Pilot evaluating
  energy performance indicators for energy-efficient PT infrastructure in Maribor & assessment of pilot transferability & replicability
  (10. 2021)
Purchase in 2021?, Evaluation report (03.2022)
CIVINET WEBINAR, 19.5.2021

## Slide 16
E-bus – comparison of technologies
CIVINET WEBINAR, 19.5.2021
Invertni pantograf (Panto down) | Pantograf na busu (Panto up)
1 Teža kontaktnih sani na e-busu ~7kg 2 Manj stroškov vzdrževanja avtobusa, vzdrževanja pantografov zunanji izvajalec 3 Cenejši avtobus, dražja polnilnica (170-210k€) 4 Ob nedelovanju pantografa, se avtobus polni na bližnjem pantografu 5 Kontaktne sani na e-busu so lahko katerekoli znamke/proizvajalca | 1 Teža pantografa na e-busu ~60kg 2 Večji stroški vzdrževanja avtobusov, vzdrževanje pantografov v delavnici 3 Cenejša polnilna postaja (130-160k€), dražji avtobus 4 Ob nedelovanju pantografa je avtobus neuporaben. 5 Pantograf na avtobus mora biti kompatibilen z infrastrukturo
Poznamo dva načina hitrega polnjenja:

## Slide 17
E-bus – selected option for Maribor
CIVINET WEBINAR, 19.5.2021

## Slide 18
CIVINET WEBINAR, 19.5.2021
E-bus – selected option for Maribor

## Slide 19
E-bus – comparison of technologies
CIVINET WEBINAR, 19.5.2021
Strategija polnjenja | Počasno (v delavnici) | Priložnostno polnjenje (v delavnici in čez dan)
Tip polnjenja | Delavnica: od 35 do 150 kW | Delavnica: od 35 do 150 kW Priložnostno: od 150 do 600 kW
Čas polnjenja | Delavnica: od 3 do 10 ur | Delavnica: od 3 do 10 ur Priložnostno: do 10 minut (na postaji)
Profil polnjenja (poenostavljeno) |  | 
Doseg | 100-200 km na dan | 200-500 km na dan
Stroški | 1 Višji stroški baterije 2 Cenejša polnilna infrastruktura | 1 Nižji stroški baterije 2 Dražja polnilna infrastruktura 3 Višji stroški vzdrževanja
Glavne razlike med nočnim in priložnostnim polnjenjem

## Slide 20
Current research
Simulation of driving cycle on line 6
Technical feasibility studies for e-bus charging infrastructure and E-buses
Investment documentation for 5 e-buses (12 m) and 3 e-fast Opp chargers
100 kWh batteries/ 200 kW e-chargers
Speed diagram
Latitutde
Vehicle parameters
GPS/GPX localisation
Matlab Simulation
Speed, Tourqe,
Power and battery size needed
with recuperation
CIVINET WEBINAR, 19.5.2021

## Slide 21
E-bus – now, 2021
city centre mini e-bus (since 2017), 3 in operation in 2021
CIVINET WEBINAR, 19.5.2021

## Slide 22
E-bus – now, 2021
public procurement for 5 full electric buses, JUNE 2021
Public procurement for 2 fast charger 150kW and 300kW, JUNE 2021
CIVINET WEBINAR, 19.5.2021

## Slide 23
Thank you for your attention!
Aleš KLINC
ales.klinc@maribor.si
CIVINET WEBINAR, 19.5.2021